## Slide 1: Renewable Survey for Ashton Hayes

## Slide 2: Overview
What are the next steps for renewables in Ashton Hayes?
On individual or community buildings
Look at the products
Cost and installation process on a community scale?

## Slide 3
Photovoltaics
Wind
Anerobic digestion
Hydro
Biomass
Types

## Slide 4
Bulk installation across the village will allow reduction in costs.
Needs management – e.g. ‘village marshal’ to let workers in and out of houses if owners are out during the day – same for retrofitting work.
70 installations with a total capacity of 210kW would generate around 167MWh per year.
Joint planning application
Show planners that this is what the village wants.
Bulk PV installation

## Slide 5
Should be acceptable in the conservation area.
Some even better ‘mimic’ than the example.
One product made from recycled battery plastic.
More expensive but a new roof too and can insulate.
Solar slates

## Slide 6
In investigating appropriate turbines the following was taken into account:
The efficiency of the turbine a low wind speed and its cut in wind speed
Requires 18-24 metre tower
Capital cost
The maintenance required.
Whether it is 3 phase or single phase
The noise it produces
MCS accreditations (equivalent accreditations may be allowed in future)
Wind

## Slide 7
Individuals have expressed an interest. Other potential sites are the school or playing field.
If the Gaia turbine can be run with a reduced cut-in wind speed this is the best fit to the requirements criteria.
The Eoltec is the next best fit to the requirements although less attractive in terms of cost/kWh produced.
Antaris a good option if a suitable tower height is possible – very few in the UK.
Costs are between £32 000 and £48000
6-11kW Wind Capacity

## Slide 8: Gaia 10kW
Antaris 6-9kW

## Slide 9
School or playing field are possible sites. Better value for money.
Small Antaris 2.5kW only stand alone turbine suitable
Ridgeblade roof mounted may be more suitable – currently under test.
Under 3kW
Endurance 50kW

## Slide 10
No technology available for the small streams in the village.
Will continue to investigate and monitor developments.
Hydro

## Slide 11
‘The muckbuster’ may be suitable to process a few households of waste – replace septic tanks.
May be grass cuttings as well.
Need more work into viability – John Moores University have expressed an interest..
Have to avoid ‘feast and famine’ for the bugs!
Anerobic Digestion